## Slide 2: Enhancing Device Security: Leveraging TrustMANAGER / keySTREAM solution to comply with security legislation and standards as TEC 31318 and AIS-140
Brandon Wu
Amrita Rajamani D
Notes: Welcome and Introduction of Amrita and Brandon and the topic covered

## Slide 3: Code of Practice for Securing Consumer IoT
Notes: Brandon
Introduce India Code of Practice, it provides guidelines of securing consumer IoT device.
the majority of security spec is referring to EN 303645 which is the IoT standards from UK, EU, Japan, India…
https://www.tec.gov.in/pdf/M2M/Security%20by%20Design%20for%20IoT%20Device%20Manufacturers.pdf

## Slide 4: EN 303 645 standard
https://www.etsi.org/deliver/etsi_en/303600_303699/303645/02.01.01_60/en_303645v020101p.pdf
Notes: Brandon
Key requirements:
Secure Boot
Secure OTA update
Secure Communication
Securely store sensitive security parameters (keys / certificates): Hardware key storage
EN303645, is also the standard selected by the Cyber Resilience Act (CRA) legislation in Europe. Starting 2027, any product sold in EU will have to be CRA certified. And other countries also took over EN 303645 as the standard for IoT solutions

## Slide 5: Intelligent Transportation Systems (ITS)
AIS-140
Notes: Brandon
Same as TEC 31318, the latest AIS-140 Amendment requires secure provisioning mechanism (factory or in-field) which possibility to perform secure firmware update and a secure mechanism to update keys / certificates
https://morth.nic.in/sites/default/files/Finalized_Draft_AIS_140_regarding_Intelligent_Transportation_Systems_.pdf
https://hmr.araiindia.com/api/AISFiles/Further%20Revised%20Draft%20Amendment%203-%20Part_A%20and%20B_and%20Annexure%20D%20for%20private%20vehicles_cb4c11fd-e5c8-4631-87c6-f5867979b1ec.pdf

## Slide 6: What’s Changing the Security Landscape
Security updatability driven by …
  Upcoming standards & regulations
  Segment specific: EN 303645, ISO 62443, ISO15118 / OCPP, AIS-140…
Customers are seeking to add differentiation to their products
  Security “quality” labels : standards & legislation intends to push manufacturers
  to maintain security for the expected product's lifetime
  Need to personalize end customer's user experience
Logistics to deploy secrets
  How to deploy and update new keys in existing devices
  Need to connect factories to key management cloud platform cost efficiently
Notes: Brandon

## Slide 7: EN 303645 Use Cases vs Crypto Asset Requirements
Use Cases | Requirements | 
 | Infrastructure / Cloud | Device
No universal default password | n/a | Unique Serial Number (immutable) Unique Private key
Software Integrity (Secure Boot) | Private Key | Public Key
Secure Firmware Update | Private Key Firmware delivery mechanism | Public Key
Secure Communication (Custom PKI) | Root CA Private Key | Root CA Public Key Device Unique Private Key Device Certificates
Credential / Data in-field management | Root of Trust | Root of Trust
Notes: Brandon
EN303645 use cases requires some crypto assets to be securely generated and stored in the infrastructure (HSM), then leveraged in the Cloud and in the connected product. It’s all about keys (Private or Public), certificates, and Root of Trust

## Slide 8: Hidden Costs of Security
Item | Costs
Infrastructure | HSM Software Platform and Integration Training Certifications
Infrastructure Maintenance | Annual costs (training, certifications, continuous improvement…)
Root CA | Creation Annual Secure Hosting (during project lifetime)
Provisioning | In-factory In-field: Embedded Firmware + Cloud development + Cloud Platform
In-field Key management | Embedded Firmware + Cloud development
Notes: Brandon
Embracing security requires heavy investment in secure infrastructure and management of the provisioning
Infrastructure: 500k$
Infrastructure Maintenance: 50 to 100k$ per year over product lifetime
Root CA / Root Keys creation (25k$) and hosting over product lifetime (25k$)
Provisioning (Secure Programming):
1$ per unit for factory provisioning
0.5$ per unit for in-field provisioning (+ Embedded Firmware / Cloud development: 4 men-year)
Key management / rotation / revocation: 0.3$ per system per update

## Slide 9: Current challenges with credentials in embedded systems
During development, manufacturing, shipping
and in the field

## Slide 10: The challenges to secure embedded devices
Implement Foundational security at scale
lifecycle management
provision unique, trusted identities per device
Generate a CHAIN OF TRUST and attach every devices to it
Personalization at manufacturing and NEVER expose the private keys
HOW to do it correctly?
?
Notes: Brandon
  The biggest barrier to deploying IoT projects is providing robust security that can be scaled for a large number of devices.
  The core security challenges are device personalization and lifecycle management.
  IoT devices need to be provisioned with unique, trusted identities .
  Typically, this involves generating a Root CA and provisioning each device with the unique identity linked to the Root CA
  This needs to be done at the manufacturing step and should NEVER expose the secret keys at any step in the process.
  So the question is HOW to do it correctly?

## Slide 11: The problems are with the keys
CREATION
MANUFACTURING
DEPLOYMENT
MAINTENANCE / LIFECYCLE
RETIREMENT
Notes: Brandon
During all aspects of the product lifecycle

## Slide 12: What happens to my keys ?
How do I create development keys?
What happens to my development keys ?
Can I use my development device and move it to production device ?
Are your keys accessible to devices you are shipping ?
Can the key be copied ?
Are you keys accessible from the device ?
How do you create production keys ?
Where are your device, intermediate and root keys securely stored
Can the key be copied ? Who has access to your keys ?
MANUFACTURING
DEVELOPMENT
SHIIPPING
IN THE FIELD
Notes: Brandon
In different stage, there will be different challenges to manage the keys

## Slide 13: Simply put …
… needs to have security updatability and/or management capabilities
One asset… that moves across time
… and/or space
… has multiple or different ownerships throughout its life cycle
Notes: Brandon
Knowing that asset can move across time / space, can have multiple owners that requires a way to remotely and securely manage credentials.

## Slide 14: Objectives
Notes: Brandon

## Slide 15: What is this class about ?
Self-service custom PKI in seconds
Certificate expiration date management
Certificate update
Certificate revocation and renewal
Transfer of ownership
Notes: Brandon
Understand what is keySTREAM and Trust Manager, what is a PKI and how to create it on keySTREAM, how to manage / update / revocate / renew certificates and how to transfer the ownership of the device.
All keySTREAM logos approved by Kudelski

## Slide 16: You will learn
How keySTREAM and ECC608 TrustMANAGER helps
To create a proper certificate chain that endures time
To keep embedded security up to date
Helps your company to provide better end user experience
Helps your company with new business model(s)
Can lower cost, development time and complexity
Manage the lifecycle of cryptographic credentials
Notes: Brandon

## Slide 17: Where does TrustMANAGER help ?
Security standards and legislations requires to keep your security up to date
Track what is where and when, who has it
Manage multiple patient for a single device
Medical
Fleet Management
IoT
Building Access
Short term rental
Long term rental
Hotel, universities, corporate
EV Charging Stations
ISO15118 / OCPP standards
Certificate rotation is specified
Asset Management
In-field ownership setup and management
Inventory Management
Pay-as-you provision
Lease model
Warranty/return management
Governed by IEC62443
Improve Installation and deployment
Industrial
Notes: Brandon
TrustMANAGER is a security solution that can help to enable true security in different type of markets, mainly for connected products, and stick to legislation / standards.
IoT: EN 303645, CRA
Fleet Management: AIS-140

## Slide 18: Security Across the Product Lifecycle
Standards requires Product Manufacturers to implement & maintain security across the lifecycle
Concept Prototyping
Cybersecurity requirements
Cost & Time constraints (Iron Triangle)
Development
Crypto Asset generation
Software integration
Production
Key and Certificate provisioning
Distribution and logistics
Utilization
Support
Retirement
Cloud integration
Threat Analysis
End user activation
Operation
Software update
Vulnerability management
Sensitive data management
Sensitive data handling
Device recovery & repurpose
Hardware integration
Notes: Brandon
Standards as EN 303645 and AIS-140 requires product manufacturers to implement security throughout the lifetime of the product, from concept to retirement. This includes threat model, generation of Root keys for development and manufacturing, secure programming (aka provisioning), product installation and management, support (as firmware update and vulnerability management).

## Slide 19: Trust Manager / keySTREAM : Across the Product Lifecycle
Concept Prototyping
Development
Production
Utilization
Support
Retirement
Use Cases
(C source code examples)
Root CA / Root Key(s) generation
In-field provisioning
Key(s) / Certificate rotation
Data Provisioning
Code Signing
FW update
Access Management
Key(s) / Certificate revocation
Root CA / Root Key(s) secure storage (Maintenance)
Notes: Brandon
Trust Manager helps to support all major steps of the product lifecycle, by providing secure silicon, generation and hosting of Root keys, in-field provisioning and remote key / certificate management as well as code signing and secure OTA firmware update

## Slide 20: Agenda
What topics will be approached
Notes: Amrita

## Slide 21: Agenda
Root CA and custom PKI
In-field provisioning
Certificate management
Notes: Amrita

## Slide 22: Preliminary setup
Notes: Amrita

## Slide 23: Development kit
Onboard debugger
(nEDBG)
EV10E69A
SAMD21 ARM® Cortex ® M0+
ECC608
Secure Authentication IC
mikroBUS
WiFi click7 (WINC1500)
mikroe.com
Notes: Amrita
Our evaluation is supported by a main board that includes a SAMD21 CortexM0+ MCU with and ATECC608 Secure Element (TrustMANAGER flavor), a Wifi7 click board from mikroE. Such hardware will be securely connected and authenticated on keySTREAM SaaS (Security as a Service) solution from Kudelski, and we will use AWS as an Application Cloud
All Kudelski IoT Things logo approved by Kudelski

## Slide 24: Security : It’s All About the Key
“A cryptosystem should be secure if everything about the system, except the key, is public knowledge”
  Kerckhoff’s Principle
  We use industry standard algorithms, and we protect the key from being accessed and exposed
Notes: Amrita
As seen previously, all standards / legislation relies on know cryptosystem and the capability to securely store the keys without ever exposing them outside the secure vault.

## Slide 25: What is a root CA ?
It’s the highest authority in a certificate chain
It’s self-signed (give itself its own identity)
Its value is the highly sensitive
Some companies with highly critical system prefers to have it off-line.
Its private key is paramount and must be protected in an HSM
Kpub
Kpriv
Signs its own public key
Notes: Amrita
Secure cloud authentication is generally based on a Custom PKI (Public Key Infrastructure) on which we have the notion of Root Certificate Authority (root CA).
The Root CA is the highest authority in the Custom PKI, and is a very high value in securing the whole system. Root CA private key should be securely stored during the product lifetime, and is generally only used at the beginning of the project to generate all intermediate Certificate Authority.
So if everything goes well during the production and lifetime of products, it is only used once.

## Slide 26: What can happen if you don’t protect the rootCA ?
  The rootCA private key is inaccessible or lost
  No product launch
  Production goes down
The employe responsible leaves the company, is laid off or is absent
  Open door to counterfeits
  Compromised PKI needs to be revoked. a new PKI needs to be deployed, – what’s your plan ?
  Already deployed products are not trustable
  Lost of trust in manufacturing
The rootCA private key is stolen
  No product launch
  Production stops
  Already deployed products are not to be trusted anymore
  A new PKI needs to be deployed
You lose the private key because it’s in a USB stick or hard drive
  No more intermediate certificate creation for manufacturing, line down
  Service outage
There was a problem, you need to access the rootCA private key, it’s nowhere to be found
Notes: Brandon
Root CA private key shall be securely stored and never exposed. We have seen several cases where it was exposed, leading to vulnerability of the entire fleet of product.
It can be due to the fact that the employee in charge of the Root CA is leaving the company, or to the fact that the Root CA private key is stolen or lost.
In some special cases, manufacturer will need to access the Root CA private key to generate new intermediate signers. Hence the need to protect it for the lifetime of the project

## Slide 27: Custom PKI
Intermediate certificate*
Device certificate
Device certificate
Device certificate
Root CA
With customized Company Name and Organization fields
With customized Company Name and Organization fields
Notes: Amrita
This is a typical example of a Custom PKI with a root CA, intermediate CA and device certificates.
Root CA will sign the Intermediate CA - it will basically delegate its authority to the Intermediate CA which will sign device certificates (unique per device)

## Slide 28: Custom PKI scales your ecosystem
Root CA
Product Line 2
Product Line 3
Device certificate
Device certificate
Device certificate
Device certificate
Device certificate
Device certificate
Device certificate
Device certificate
Device certificate
Product Line 1
ICA1
ICA2
ICA3
Lots of private keys to protect
Notes: Amrita
This is a second example of a custom PKI, with the Root CA signing different intermediate CA. It can be used to differentiate different product lines, knowing that only the Root CA will be able to authenticate each unique device certificate.
It’s also a way to manage different manufacturing location or to manage 3rd-parties who will be able to produce end products on behalf of the product manufacturer.

## Slide 29: This is a root certificate
Version
Certificate S/N
Cert Algorithm Identifier
Cert Authority Signature
Issuer
Validity Period
Subject
Public Key
CA’s Signature Data
HSM Issuer Unique ID
Subject Unique ID
Extensions
Subject where CN+O
Who you are
Issuer
Who signed you
CN : Common Name
O : Organization Name
(C : country)
Notes: Amrita
This is an example of the Root certificate. It shows that one can customize the Common name and the Organization name.

## Slide 30: Creating the certificate chain
How can the private key be trusted
Root Public Key
Root Private Key
Intermediate
Certificate Public Key
Device Public Key
Intermediate
Certificate Private Key
Device Private Key
Calculated
Calculated
Calculated
Root Kpriv signs root Kpub
Root Kpriv signs Intermediate Certificate Kpub
Intermediate Certificate Kpriv signs device Kpub
Notes: Amrita
To create a Custom PKI with associated certificate chain, first the Root CA Private key need to be generated. It will then sign it’s corresponding public key. From their, the Root CA PrivK will sign the Intermediate CA certificate and the Intermediate PrivK will sign the device Public key. Such signatures can happen during factory secure provisioning or during in-field secure provisioning.

## Slide 31: Certificate Verification
Host
Subject
Certificate
Authority Info Certificate Info
Subject Info
Subject Public Key
Signature
Authority
Public Key
Private
Key
Public
Key
Verify
(ECDSA)
TBS (To Be Signed)
OK?
Notes: Amrita
Once all signature are done, and the product is connected, products can start authentication by verifying the certificate chain. Public Keys are leverage for this process,

## Slide 32: Custom PKI authentication process
Verify Signer
Public Key
Verify Device
Public Key
Challenge /
Response
Intermediate Certificate
Signature
Signer Public Key
Device Certificate
Signature
Device Public Key
ECDSA
Verify
Intermediate Certificate
Signature
Signer Public Key
OK?
Root
Public
Key
ECDSA
Verify
OK?
Device Certificate
Signature
Device Public Key
Device
Private Key
ECDSA
Sign
Random
Challenge
ECDSA
Verify
OK?
Cloud
Device
Notes: Amrita
Once all signature are done, and the product is connected, products can start authentication by verifying the certificate chain. Public Keys are leverage for this process – Device will provide its Intermediate Certificate to the Cloud that holds the Root CA Public Key – through an ECDSA verify cryptographic function, it will verify the authenticity of the Intermediate certificate. Once verify, the device will provide its device certificate which will be verify against the Intermediate CA public Key. The last process will be for the Cloud to send a random challenge to be signed by the device private key. Once returned, the Cloud will verify this signed challenge with the device public key (previously authenticated). If the verification is successful, the Cloud will then allow the device to connect and will setup the secure channel.

## Slide 33: Certificate Authentication
Host
Subject
Certificate (Verified)
Authority Info Certificate Info
Subject Info
Subject Public Key
Signature
Challenge
(Random)
Sign
(ECDSA)
Verify
(ECDSA)
Signature
OK?
Certificate
Authority
Public Key
Private
Key
Public
Key
Notes: Amrita

## Slide 34: Protecting the keys in the certificate chain
At every instance of the chain, the private key MUST be securely stored
Use HSMs for private keys in the cloud
Use HSMs for private keys in manufacturing
Use CryptoAuthentication ™ IC in embedded systems
Private key is paramout
MUST BE PROTECTED
Notes: Brandon
It is, of course, extremely important that these private keys, especially the root CA private key, remain inaccessible when they are not needed by the manufacturer. To ensure this, keySTREAM provides a Hardware Security Module (HSM) service that protects these keys so the root CA private key is protected during the lifetime of the project.
This is the keySTREAM Root CA as a service fonctionnality
And the device private key is kept in secure storage on the device in the field.

## Slide 35: Root CA and PKI by Kudelski IoT
Setup your custom rootCA
Self-service custom PKI in seconds
Private key in your HSM space within Kudelski secure infrastructure
Notes: Amrita
keySTREAM allows customers to setup their own custom root CA that will be secured during the project lifetime in HSM within Kudelski secure infrastructure. Let’s recall that Kudelski is in the business of secure credential since decades, mainly through their pay TV solutions.

## Slide 36: Self-service keySTREAM PKI w/ Root CA
 | DIY | w/Large RootCA providers | w/ keySTREAM
Onboarding | Manual | Custom | Self Service
Learning curve | High | Medium | Low
Implementation time | Months | Weeks | Minutes
Maintenance | Manual, Expensive | Expensive, add-on | Automated
Availability | Poor | 99.9x% | (min) 99.9%
Backup (Redondance) | None | Expensive | Affordable
Price | Unpredictable | $25k – $100k (rootCA only) | $5k fee + $5k/y (fully managed PKI)
Security | None to average | High | High
Notes: Amrita
For sure, customer can choose to
Setup their own Root CA and maintain it over the product lifetime. It requires heavy investment in dollar and engineering resources, and the level of security will be limited (unless investing 500k to 1M$)
Leverage 3-parties specialized in Root CA creation and hosting. Here, the security level and availability will be high, but the associated price will also be high. It will also not come with any provisioning services / secure implementation between the SaaS and the embedded device.
Leverage keySTREAM ready-to-use service which comes at a very affordable cost and with built-in additional paid services as in-field provisioning and credential update / management. Reason why keySTREAM is so competitive is because Kudelski / Microchip offers a complete solution for low to high volume customers. The infrastructure is already amortized following years of investment and being operate for high volume customers since then.

## Slide 37: Setting up your rootCA and custom PKI
Device
TrustMANAGER
KTA
Host Platform, OS and Applications
Host Applications
CryptoAuthLib
keySTREAM Service
Customer managed PKI
Sign device certificates (online CSR)
1. Device is onboarded and certificate is provisionnned.
Sign intermediate CAs (offline CSR)
Device signing CA
Intermediate CA
Setup, customer register its CA in its device management platforms.
2. Device connect to customer Device Mgt platform using device ECC608 private key and its certificate. Device is authenticated by registered CA.
keySTREAM
Root CA
Notes: Amrita
So the first operation here is to setup the Root CA and the Custom PKI. Basically, the Root CA is the Master authority that will delegate the authority for the Intermediate CA to generate end product unique certificates.
Through keySTREAM, you generate your root CA and the intermediate CA which is related to a given fleet profile. For example, a customer have Product A, B and C, which correspond to 3 different fleet profile (as maybe the host MCU is different or just the embedded firmware is different. Customer will likely use the same Root CA but different Intermediate CA and fleet profile. This will allow customer to manage each fleet of devices and associated credentials / firmware separately.

## Slide 38: Root CA and custom public key infrastructure (PKI)
Setting the chain of trust
Notes: Amrita / Hands-on: create a Root CA / Custom PKI in Keystream
Log into keySTREAM
Create the Root CA
Creation the Fleet Profile
Create API key

## Slide 39: Let’s implement your rootCA and custom PKI in keySTREAM
Notes: Amrita / Hands-on: create a Root CA / Custom PKI in Keystream
Log into keySTREAM
Create the Root CA
Creation the Fleet Profile
Create API key

## Slide 40: Protecting the key in the device
Notes: Brandon

## Slide 41: Who needs a self-service PKI w/ Root CA
If you don’t have a foundational level of security expertise and are short of time, resources and budget
For companies subject to security standards and regulations
If you want to scale your fleet of products effectively
If you care about the longevity of your devices across time

## Slide 42: keySTREAM offers automation for authentication
Certificate Management
certificate templates definition
generation of standalone certificates or batch certificates
management of the issued certificates (i.e. monitor, revoke, re-key).
CA management
Users can configure the issuing CA for a specific organization.
Multi-tenancy
Role Based Access Control (RBAC) for the users of PKIaaS and organization management.
Log auditing
Each operation in KeySTREAM is logged (i.e. user login, certificate request, certificate generation, etc).
Public/Private cloud integration
integrates with public cloud services like AWS IoT Core and Azure DPS/IoT hub or private clouds
APIs support
RESTful APIs and technical documents are available for automating the certificate enrolment process and managing the life-cycle of devices.
Client library support
Client library (KTA) is tiny (<10KB) and integrated in Microchip Harmony

## Slide 43: What is a CryptoAuthentication IC?
Crypto
Engine
ECC608
I2C or Single Wire
How the Microcontroller communicates to the secure element?
CryptoAuthLib library
MCU or MPU or
Cloud server
Random Challenge
Response
CryptoAuthLib
Secret Key
A vault that protects secrets,
A companion device to the microcontroller
Inside the vault secrets are generated during manufacturing - inside Microchip factories
Keys, certificates are never exposed and handled by Microchip secure provisioning process
All done safely inside a persistent-secure hardware protected device
Notes: Brandon
Each device will have a unique Private key that needs to be protected for the lifetime of the project. Secure Element as ECC608 are designed to protect key(s) and never exposed them.

## Slide 44: Rate the way you protect keys
Common Criteria JIL rating
Notes: Brandon
JIL is an internation standard way to rate the level of protection of the keys inside a Vault. It is largely used by the community. It requires to go through an independent 3rd-party lab that will assess potential vulnerability and related efforts to retrieve a key. Being rated JIL high means that the 3rd party was not able to find a vulnerability during the given time-frame.

## Slide 45: ECC608
Features and Memory
Command | Description
Cryptography | ECC-P256 and ECDSA sign/verify, ECDH SHA256 & HMAC AES128 encrypt/decrypt PRF/HKDF calculation for TLS1.2 & 1.3
Vulnerability resistance | High per the JIL standard
EEPROM | 10kbits
Counter | Up to 2,000,000
Serial Number | 72 bits
RNG | NIST SP800-90
I/O | I2C, SWI
Supply Voltage | 2.0V – 5.5V
Sleep current | 30 nA Typical
Temperature | -40°C to 85°C Extended temperature up to 100°C
Compliance | NIST CAVP and ESV algorithm certified
Packages | uDFN8, SOIC8, 3pin RBH, WCSP, die
Data zone | Slot0-slot7 (36 bytes each) Slot8 (416 bytes) Slot9-slot15 (72 bytes each)
  Trust Platform availability
  Trust&GO ATECC608-TNGTLS
  TrustMANAGER ECC608-TMNGTLS
  TrustFLEX ATECC608-TFLXTLS and ECC608-TFLXWPC
  Trust CUSTOM ATECC608-TCSM
  Library
  CryptoAuthLib
  Extensive Security Measures including:
  Active Shield to protect against invasive attacks
  Internal Memory Encryption and Scrambling
  Low and High supply voltage Tampers
  Low and High temperature Tampers
Commands overview |  |  |  | 
GenKey | Counter | Lock | SHA | Read
Write | AES | CheckMac | Derivekey | ECDH
GenDig | KDF | MAC | NONCE | PrivWrite
Random | SecureBoot | UpdateExtra | Verify | 
Production
Notes: Brandon
Provide high level information on ECC608

## Slide 46: TA101-VAO
Features
Command | Description
Cryptography | ECC-P256/P384/P521 and ECDSA sign/verify, ECDH SHA256/SHA384/SHA512 & HMAC AES128, AES256 encrypt/decrypt, Fast CMAC PRF/HKDF calculation for TLS1.2 & 1.3 Up to RSA 4k KeyGen/Sign/Verify, Encrypt/Decrypt bitcoin ECC curve Brainpool Edward Ed25519
Vulnerability resistance | High per the JIL standard
EEPROM | 11 kBytes, field upgradable
Counter | Yes
Serial Number | 72 bits
RNG | NIST SP800-90
I/O | I2C, SPI
Supply Voltage | 2.7V – 5.5V
Temperature | Automotive AECQ-100 grade 1 -40°C to 125°C
Certification | FIPS 140-3 level 2, with physical security level 3
Packages | SOIC8, VQFN-24
  Optimization
  Automotive qualified Trust Anchor
  Reduced time to market adding security with minimal impact to existing designs
  Reduced risk with pre-provisioned security code and tested by 3rd party vulnerability assessments
  Reduced overall cost avoiding more expensive customized MCU's and 3rd party SW
  Libraries
  CryptoAuthLib
  AUTOSAR
  Extensive Security Measures including:
  Active Shield to protect against invasive attacks
  Internal Memory Encryption and Scrambling
  Low and High supply voltage Tampers
  Low and High temperature Tampers
Commands overview |  |  |  | 
AES | Authorize | Counter | Create | Delete
DevUpdate | ECDH | Export | Lock | MAC
ManageCertificate | Power | Random | Read/Write | RSAEncrypt
SecureBoot | SecureBoot | SelfTest | SHA | Sign/Verify
Production
Notes: Brandon

## Slide 47: How Keys Are Protected Matters!
Strong Multi-level HW Security
  Active shield over entire chip
  All memories internally encrypted
  Data independent crypto execution
  Randomized math operations
  Internal state consistency checking
  Voltage and temperature tampers
  Internal clock generation
  Secure test methods, no JTAG
  No debug probe points, no test pads
Designed to Defend Against
  Microprobe attacks
  Timing attacks
  Emissions analysis attacks
  Fault, invalid command attacks
  Power cycling, clock glitches
SPG Crypto Devices
Standard
Devices

## Slide 48: Inside the CryptoAuthentication IC
48
Secure Key Storage
CryptoAuthentication IC
Cryptographic algorithm
Unique Serial Number
HW protection
Random Number Generator
Unique identity
Protected KEYs for a lifetime
Cryptographic acceleration
Scrambled and encrypted memory
Monotonic counters
Random Number Generator
Monotonic Counter
Notes: Brandon

## Slide 49: Comparisons for root CA and PKI options
 | Trust&GO | TrustMANAGER | TrustFLEX | DIY
Root CA certificate and private key | Static key owned and created by Microchip in our factory HSM Default fields will be the same for everyone. Certificate cannot be customized. | Custom & Managed rootCA by keySTREAM Self service from keySTREAM RootCA created under KeySteam HSMs, managed by you | Customers are required to maintain their own keys, usually done through 3rd party CAs which can be very expensive Or Use MCHP rootCA and default static signer certificate | Requires a high level of technical knowledge, secure systems and policies to securely manage Root CA key and certificates.
Signer certificate and private key (ICA) | Signed by Microchip root at Microchip secure facility Certificates/keys are static | N/A | Signed by Microchip root at Microchip secure facility | Generally, no protection if keys are not stored on HSMs
Device certificate and private key | Certificates/Keys securely stored in Microchip CryptoAuthentication IC | Custom Device certificate signed by RootCA. Certificates/Keys securely stored in Microchip CryptoAuthentication IC | Certificates/Keys securely stored in Microchip CryptoAuthentication IC | Generally, no protection if keys are not stored on HSMs
Notes: It is, of course, extremely important that these private keys, especially the root private key, remain inaccessible when they are not needed by the manufacturer. To ensure this, Microchip provides a Hardware Security Module (HSM) service that protects these keys.
The root private key is protected by Microchip in our HSM.
We can assist a customer in enabling their own HSM that protects their signer private key.
And the device private key is kept in secure storage on the device in the field.

## Slide 50: Let’s implement your rootCA and custom PKI in keySTREAM
Notes: Amrita / Hands-on: create a Root CA / Custom PKI in Keystream
Log into keySTREAM
Create the Root CA
Creation the Fleet Profile
Create API key

## Slide 51: Current friction points when loading keys in ICs
Provisioning of the birth certificate private key without a CryptoAuthentication breaks the trust in the certificate chain.
True when using 3rd party rootCA service without secure element OR using cloud “provisioning” services
Uploading large quantity of device certificates and public keys in the cloud platform
At production scale, the upload time needs to be small
Who upload them needs to be controlled ?
Inventory challenges due to custom part numbers
Keys are unique per devices creating silicon customization
Customization in manufacturing creates inventory challenges
Supply chain challenges
Contract manufacturers
Notes: Brandon

## Slide 52: When to provision custom keys in embedded systems ?
Customization during
manufacturing of the silicon
Customization when the device
is deployed in the field
Notes: Brandon

## Slide 53: Trust Platform : factory provisioning services
Pre-configured | YES | YES | YES | NO
Provisioning | Zero touch (at Microchip) | Zero touch (In-field) | Custom (at Microchip) | Custom (at Microchip)
Complexity | Lowest | Lowest | Lower | Custom
Secrets | Static by Microchip | Managed SaaS | Static by Customer | Custom
Low MOQ Flow | 100 units | 2000 units | 2000 units | 4000 units
High Volume Flow | Starting 30ku | Starting 30ku | Starting 30ku | Starting 30ku
Use cases | Any Cloud TLS LoRaWAN Crypto Mining – Helium | Root CA services Any Cloud TLS FOTA Key rotation Data | Any Cloud TLS Firmware Verification Key rotation Wireless charging Secure Boot Local authentication | Any custom use case(s)
Devices | ATECC608 for TLS ATECC608 for LoRa SAMA5 Wireless SOM WFI32E01PC – Wifi+MCU+ECC608 ECC608 for Helium | ECC608 | ATECC608 TLS ECC608 WPC PIC32CM (MCU+SE) ECC204 AUTH TA010 AUTH ECC204 WPC TA010 WPC SHA104 AUTH CEC1736 | ECC608 ATSHA204A TA100 dsPIC33CK (MCU+SE) CEC1736 TA101
Notes: Brandon

## Slide 54: TrustFlex / TrustCustom Factory Provisioning
Concept Prototyping
Development
Production
Utilization
Support
Retirement
Use Cases
(C source code examples)
Root CA / Root Key(s) generation
Factory Provisioning
Key(s) / Certificate rotation
Data Provisioning
Code Signing
FW update
Key(s) / Certificate revocation
Root CA / Root Key(s) secure hosting
Customer
Notes: Brandon

## Slide 55: Trust Platform : in-field provisioning services
Pre-configured | YES | YES | YES | NO
Provisioning | Zero touch (at Microchip) | Zero touch (In-field) | Custom (at Microchip) | Custom (at Microchip)
Complexity | Lowest | Lowest | Lower | Custom
Secrets | Static by Microchip | Managed SaaS | Static by Customer | Custom
Low MOQ Flow | 100 units | 2000 units | 2000 units | 4000 units
High Volume Flow | Starting 30ku | Starting 30ku | Starting 30ku | Starting 30ku
Use cases | Any Cloud TLS LoRaWAN Crypto Mining – Helium | Root CA services Any Cloud TLS FOTA Key rotation Data | Any Cloud TLS Firmware Verification Key rotation Wireless charging Secure Boot Local authentication | Any custom use case(s)
Devices | ATECC608 for TLS ATECC608 for LoRa SAMA5 Wireless SOM WFI32E01PC – Wifi+MCU+ECC608 ECC608 for Helium | ECC608 TA101* | ATECC608 TLS ECC608 WPC PIC32CM (MCU+SE) ECC204 AUTH TA010 AUTH ECC204 WPC TA010 WPC SHA104 AUTH CEC1736 | ECC608 ATSHA204A TA100 dsPIC33CK (MCU+SE) CEC1736 TA101
* planned
Notes: Brandon

## Slide 56: Trust Manager: Across the Product Lifecycle
Concept Prototyping
Development
Production
Utilization
Support
Retirement
Use Cases
(C source code examples)
Root CA / Root Key(s) generation
In-field provisioning
Key(s) / Certificate rotation
Data Provisioning
Code Signing
FW update
Access Management
Key(s) / Certificate revocation
Root CA / Root Key(s) secure storage (Maintenance)
Notes: Brandon

## Slide 57: In-Field Provisioning
Notes: Amrita

## Slide 58: In-field provisioning comparisons
 | DYI | w/Large RootCA provider | w/ keySTREAM
Provisioning | At the CM | Birth key at CM | Automated in-field
HSM infrastructure | None or not scalable, poor maintenance | Scalable and maintained | Fully scalable and maintained
Development time | Years, dedicated to large volume | Months | Reduce time from manufacturing, get the IC faster, for all volumes
Exposure to CMs | High dependance to CM | Birth certificate/keys are exposed | Fully isolated
Control of the keys | The CM | Your company / The CM | Your company
Pricing | High and fixed by the CM | High and often prohibitive | Pay-as-you use to provision your ICs

## Slide 59: Where does keySTREAM fit ?
keySTREAM
Trusted
Agent
ECC608
Root of Trust
keySTREAM Service
Manage customer:
Custom PKI
Keys and Certificates
Trusted Public Keys
Shared Symmetric Keys
Secure Data and Configuration
Signing Services for PKI and secret keys
Notes: Amrita
keySTREAM is a Device Security Management Platform to secure your device identity, connections, data, firmware and more using Microchip TrustMANAGER Root of Trust. The root of trust is securely injected during the manufacturing of the silicon, making this solution fully secure until it is provisioned with customer custom secrets (keys, certificate, data…). The root of Trust also allow to ensure a secure binding between the Secure Element (the embedded system) and the security platform for the lifetime of the product.

## Slide 60: In-Field Provisioning and Extra Services
Customer Device Certificates
Root of Trust
Customer
Issuing CA
Customer
Root CA
ATECC608
Trust&GO Managed
registered
ATECC608
Trust&GO Managed
keySTREAM
in-field provisioning
MCHP chip secure identity
MCHP Root CA
Manages customer credentials for,
Different communication protocol; HTTPs, MQTTs, CoAP, SFTP, …
Different Cloud services; Azure, AWS, Private Cloud, …
Different Local services, networks and servers.
Can be deployed on,
Different network protocols;
Wifi, Ethernet, LTE, BLE…
ECC608-TMGNTLS
ECC608-TMGNTLS
Field
Notes: Amrita
Microchip provisions a unique Root of Trust in each compatible secure element. keySTREAM authenticates the secure elements using the RoT and enables in-field provisioning of new credentials and manages their lifecycle.
It also allows to automatically register onboarded device in any Cloud through any communication protocol and network protocol.

## Slide 61: keySTREAM late provisioning overview
Field
Customer Factory
keySTREAM Service
MCHP
keySTREAM account setup
Secure Connections / in-field provisioning / in-field credential management.
TrustMANAGER ordering
Notes: Amrita
This is the high level flow from when the ATECC608 Secure Element is produced and securely provisioned with it’s unique Root of Trust up to when it is securely customized in the field with customer credentials.

## Slide 62: Setup and Production
Field
Customer Factory
keySTREAM Service
MCHP
3. Customer registers TrustMANAGERs in keySTREAM to claim ownership.
This phase is not mandatory if the TrustMANAGERs were ordered to a registered MD purchaser.
2. Customer order TrustMANAGERs,
From a registered MD purchaser.
Or from any supplier.
1. Setup - customer,
creates a keySTREAM account,
creates a new configuration in keySTREAM fleet profiles,
build a device firmware with KTA and the fleet profile identifier.
Notes: Amrita
To enable the solution, here are the 3 steps to perform before being able to in-field provision the devices:
Setup the keySTREAM account, create the Root CA / intermediate CA / Fleet profile… and any credential needed to be provisioned (symmetric key, public key…). On the embedded firmware side, customer will have to integrate the KTA (keySTREAM Trusted Agent) that will contain the fleet profile Uid – KTA can run on any MCU / MPU of the market, is free of charge and is available in source code. To better support Microchip MCU / MPU solutions, it is available in Harmony under MPLAB.
Second step is to procure the ATECC608 Trust Manager directly from Microchip or through an authorized channel partner – Microchip will automatically push to keySTREAM the unique ID of each delivered ATECC608 so they are pre-loaded and ready to be securely onboarded
Optionally, customer can also register Trust Manager to keySTREAM, to increase the level of security in the logistic process

## Slide 63: In-Field Onboarding, Provisioning and Management
Field
Customer Factory
keySTREAM Service
Connections are secured by keySTREAM managed credentials.
Devices are assembled with claimed TrustMANAGER, KTA and customer fleet profile identifier.
1. At first Device connection, Device is Onboarded
TrustMANAGER and Device are authenticated,
Device is onboarded in customer account,
Device credentials are generated and provisioned, e.g. a device certificate, a shared secret key , a trusted public key, a secure configuration.
2. Device credentials are managed, for example, a device private key and associated certificate are renewed, a shared secret key is renewed,
a trusted public key is renewed,
a new security configuration is installed,
Notes: Amrita
At first connection, the ECC608 TrustManager will be authenticated by keySTREAM and will request its credential based on the fleet profile Uid. keySTREAM will generate unique certificates and will securely push it into the ATECC608 Trust Manager, as well as any symmetric key or public key define in the Fleet Profile.
During product lifetime, customer can request keySTREAM to rotate / renew or revoke device unique credentials (as private keys or certificate) or can push new symmetric keys or public key. As an example, customer can sign new firmware with a new private / public key pair and securely push the public key so that when firmware is about to be updated, the ECC608 can authentication the signature of the new firmware to authorize (or not) the update).

## Slide 64: Customer keySTREAM backend integration
Device fleet
keySTREAM Services
Management platforms
Mobile, Edge, servers, …
Customer services (e.g. FOTA)
keySTREAM UI
REST API
Customer
M2M
scripts
M2M
keySTREAM Operations can be requested through UI or REST API calls.
Fleet information and audits,
Get fleet inventory and fleet security states
Get device certificates
…
PKI signing services,
FOTA system for Firmware signature.
Authorization system to accesses devices or ressources.
…
Encryption services,
FOTA system for Firmware encryption, use shared secret key.
End2end data protection, use per device secret key.
…
Integration of services w/ REST APIs
Notes: Amrita
keySTREAM can be operated directly through the web portal or through REST API calls from the customer application Cloud.

## Slide 65: Embedded Architecture
keySTREAM Trusted Agent (KTA)
  CryptoAuthLib to interface with a TrustMANAGER
  Integration at the bare-metal level, without dynamic memory allocation and independent of operating system resources
  Source code will be integrated in Harmony for easier customer integration
  Once compiled with code optimization, the KTA size is a compact 13 KB code and requires a stack depth of 4.5 KB RAM
MCU
e.g. ATSAMD21E18
TrustMANAGER
Harmony
Azure, AWS RTOS, bare metal…
CryptoAuthLib
2. Use provisioned credentials with ECC608 cryptographic functions
keySTREAM Service
1. Provision and Manage credentials
KTA
Notes: Amrita
Architecture of the embedded system requires the integration of KTA (keySTREAM Trusted Agen) and CAL (CryptoAuthLib)
KTA allows message to be push from keySTREAM to the ECC608 TrustManager and CAL perform the call back functions to trigger any secure operation within the ECC608 Secure Element.
Combination of both libraries allows to in-field provision customer credentials then leverage such credentials at the application level.

## Slide 66: How keySTREAM and devices get connected
MCU
CryptoAuthLib
KTA
Customer
OS and Applications
TrustMANAGER
keySTREAM Secure Messages over
HTTP, CoAP or HTTPs
keySTREAM Service
keySTREAM use a Secure Message protocol
independent of the network transport protocol.
use state of the art NIST standardize Key Agreement and Secure Channel.
easy to integrated in Host protocol stack with trivial API, ktaExchangeMessage (KTA2keystream_in_msg, KTA2keystream_out_msg)
Different distinct network connections supported
HTTP, which is recommended for direct connections to keySTREAM.
CoAP, suitable for constrained connections or battery constrains applications
HTTPS, used for indirect connections, such as BLE with a mobile application.
Notes: Amrita

## Slide 67: Blank ATECC608 Organization
Slot 0
Slot 1
Slot 2
Slot 3
Slot 4
Slot 5
Slot 6
Slot 7
Slot 8
Slot 9
Slot 10
Slot 11
Slot 12
Slot 13
Slot 14
Slot 15
Read Only Data
Device Operation Configurations
Slot/Key Usage Policy Configurations
OTP Data
Data Zone | 
Slots 0-7 | 36 Bytes
Slot 8 | 416 Bytes
Slots 9-15 | 72 Bytes
Config Zone
128 Bytes
OTP Zone
64 Bytes
Config Zone
One-time lockable
OTP Zone
Only writable while Data Zone is unlocked; freely readable.
Data Zone
One-time lockable
Slots can be read/written, depending on slot policy – even after zone locked.
Slots can be individually lockable
Notes: Typical ECC certificate size: < 400 bytes

## Slide 68: CryptoAuthLib Library for Secure Elements
Notes: CryptoAuthLib Library is a very important part of the secure element solutions.
This library makes the secure element completely agnostic of the microcontroller and processor. From a business standpoint, it’s makes the opportunity landscape unlimited as Microchip secure element could work with the vast microcontrollers and processors in the global market.
CryptoAuthLib contains all the low level commands for the Micro to talk with the secure element via the integrated Hardware Abstraction Layer. If questions arise, call the Authentication Function Group (AFG) lead by Umberto Macri and place a Sales Force ticket with your question

## Slide 69: CryptoAuthLib
API for CryptoAuthentication Devices
Written in C, with Python extensions
Easy access to CryptoAuth family of devices
Host side crypto calculations
Certificate handling functions
Create (Certificate Sign Requests)
Save and Load
Sign and Verify
Documented on GitHub
www.microchip.com/CryptoAuthLib
Portable, powerful, extensible, easy-to-use
YouTube Tutorial

## Slide 70: CryptoAuthLib Folders
cryptoauthlib
lib
docs
test
atcacert
basic
hal
jwt
html
Library itself
  Certificate functions
  Basic cryptographic functions
  Hardware Abstraction Layers
  Java Web Token
Documentation
  index.html
Library test functions; based on Unity
** Only commonly used parts shown **

## Slide 71: keySTREAM Trusted Agent (KTA)
MCU / MPU
keySTREAM Trusted Agent
CryptoAuthLib
ECC608-TMNG
Embedded Application
I2C
Communication stack
HTTP
COAP
Custom
Wifi
Ethernet

## Slide 72: ECC608 TrustMANAGER : use cases
The device totally configured. There is nothing to setup in the device.
Managed TLS keys and certificates
Device Management
Transfer of ownership
OTA FW verification
FW version control
Enable your subscription model
User privileges
Notes: Clean up the list of use cases

## Slide 73: ECC608 TrustMANAGER Configuration
TLS private key to AWS
Authentication private key to keySTREAM
TLS ephemeral key
TLS Device certificate
TLS Signer public key
TLS Signer Certificate
Notes: Illustrate what keys can be used by customers for their applicaiton

## Slide 74: Ordering flow
Class focus on “Claim by Manifest” because the ECC608 TrustMANAGER is sold soldered down on the kit
It’s a backup flow if Autoclaim doesn’t work
“Autoclaiming” no manifest to upload in keySTREAM

## Slide 75: The Flow in Details – autoclaim (no manifest to upload)
1. Configure a device profile. A device_profile_uid is assigned
CUSTOMER Account / Tenant
6. Onboarding
Mutual authH secure channel is established using authenticated ATECC608 Attestation key. device_profile_uid and ownership of the chip are verified; chip must have been reported in ATECC608 Manifest File reporting in §1.
Device is onboarded in the customer tenant.
Customer
2. Order ECC608 - Direct Customer.
- Contract Manufacturer.
- Distributor.
4. TrustMANAGER ECC608 are delivered
7. Provisioning of a device profile,
customer_key is generated into the chip and attested.
customer_cert is created, signed by customer CA and provisioned in the chip.
Only once in the device lifetime!
MD
Specific credentials uploaded in keySTREAM.
3. ECC608 Manifest files are automatically registered in keySTREAM customer tenant.
5. Integrate KTA in device,
Set the device_profile_uid in MCU application firmware.

## Slide 76: The Flow in Details – claim by manifest
1. Configure a device profile. A device_profile_uid is assigned
CUSTOMER Account / Tenant
6. Onboarding
Mutual authH secure channel is established using authenticated ATECC608 Attestation key. device_profile_uid and ownership of the chip are verified; chip must have been reported in ATECC608 Manifest File reporting in §1.
Device is onboarded in the customer tenant.
Customer
2. Order ECC608 - Direct Customer.
- Contract Manufacturer.
- Distributor.
4. TrustMANAGER ECC608 are delivered
7. Provisioning of a device profile,
customer_key is generated into the chip and attested.
customer_cert is created, signed by customer CA and provisioned in the chip.
Only once in the device lifetime!
MD
Specific credentials uploaded in keySTREAM.
3. ECC608 Manifest files are manually registered in keySTREAM customer tenant.
5. Integrate KTA in device,
Set the device_profile_uid in MCU application firmware.
Notes: Amrita

## Slide 77: What’s happening to your private key ?
Not exposed, also true at the CM
Contrary to rootCA company and Cloud IaaS companies, the device private key is never loaded in the embedded system by a CM
The device private key is generated by the ECC608 TrustMANAGER, inside the IC and then managed by keySTREAM
Notes: Amrita

## Slide 78: Device Onboarding to Any Cloud
Device
Customer
Device Cert
Ordering
Phase
- Authenticate ATECC608.
- Authenticate attestation of the generated Device Key.
- Identify Owner and Device profile.
- Onboard Device in customer Tenant.
Onboarding to keySTREAM
- CSR, Sign new Device Cert using Customer Issuing CA
Slot 1 Attestation Kpriv
Signs slot3 Kpriv
Generate attestation.
Register Customer Issuing CA of the Device profile
Setup
Phase
<- Device Cert.
<- Issuing CA Cert.
Any cloud
Authenticate the Device thanks to registered Customer Issuing CA.
Use Device Cert to connect to customer Cloud
Secure TLS Communication is setup
Field Provisioning
Phase
Light Manifest files are registered in keySTREAM
Customer or Supplier Order ATECC608 chips in MD.
HSM
Integrate Device
FW with KTA
Store Issuing cert in MCU
Device Cert in ECC608 slot 10,11,12
-> device_profile_uid.
-> Chip S/N.
-> generated attestation.
Provisioning
Only once in the device lifetime!
Customer register or authorize a contract manufacturer or a supplier in MD.
InField
Configure a device profile
Notes: Amrita
animations

## Slide 79: How PKI can be used for Device authentication
Device
TrustMANAGER
KTA
Host Platform, OS and Applications
Host Applications
CryptoAuthLib
keySTREAM Service
Customer managed PKI
Sign device certificates (online CSR)
1. Device is onboarded and certificate is provisionnned.
Sign intermediate CAs (offline CSR)
Device signing CA
Intermediate CA
Setup, customer register its CA in its device management platforms.
2. Device connect to customer Device Mgt platform using device ECC608 private key and its certificate. Device is authenticated by registered CA.
keySTREAM
Root CA

## Slide 80: Setting up the in-field provisioning
Device
TrustMANAGER
KTA
Host Platform, OS and Applications
Host Applications
CryptoAuthLib
keySTREAM Service
Customer managed PKI
Sign device certificates (online CSR)
1. Device is onboarded and certificate is provisionnned.
Sign intermediate CAs (offline CSR)
Device signing CA
Intermediate CA
Setup, customer register its CA in its device management platforms.
2. Device connect to customer Device Mgt platform using device ECC608 private key and its certificate. Device is authenticated by registered CA.
keySTREAM
Root CA

## Slide 81: Management of certificates

## Slide 82: Why Dynamic Certificate Management ?
Security updatability in line with upcoming regulations and standards
Prevent instead of correcting or be ready to correct remotely
Enable personalized user experience (lease model, subscription model)
Security scalability and automation

## Slide 83: Expiration date expiration
Notes: Amrita

## Slide 84: Why managing the certificate expiration date ?
IT mandate
Standards
The time will come anyway
Current situation
Majority of certificates are static
Their expiration date is static
Consequences
Re-architecture of the PKI
New secret exchange
Re-design
Notes: Amrita

## Slide 85: Device renewal
Optional : rotate also the private key or not
Notes: Amrita

## Slide 86: Device refurbishing / Transfer of ownership
Remove device from current tenant (refurbish)
Install new FW with new PUID
Claim with new tenant
Device onboard to new tenant
Notes: Plan for demo of ToO by Adithya only

## Slide 87: Live Demonstration
Let us show you
Notes: Amrita

## Slide 88: Summary
Let’s recap
Notes: Amrita

## Slide 89: Key takeaways
Holistic Device Security
Secure generation and provisioning of keys and certificates
Secure management of keys/certificates throughout product lifecycle
Compliance and Standard
Helps to build secure products
Withstands security threats
Comply with industry standard and regulations
Easy to Use
User friendly
Easy integration to existing development tools
Scalable
Small scale to large scale IoT implementation
Notes: Amrita

## Slide 90: Course Survey
We appreciate your feedback
24042 SEC3 Class Survey